## Slide 1: Baltic SEA inteGrated unmanned aerial vehicLE multifunctional monitoring system for resurveying of shipping routes (SEAGLE)
M.Sc.Ing. Alexander Gamaleyev,
Project coordinator
PA Safe Steering Committee meeting
Turku, Finland, 17.05.2016
Riga Technical University Faculty of Transport and Mechanical Engineering Institute of Aeronautics

## Slide 2
EU strategy for the
Baltic Sea Region
ACTION PLAN
Policy Area SAFE, Action 2:
Many of today sea charts are based on somewhat inaccurate measurements made more than 100 years ago. In contrast, modern surveys are carried out with multi-beam echo sounders or airborne LIDAR technology and provide a detailed image of the seabed. As the size and draught of vessels is increasing, shoals and shallow areas which used to be below the reach of ships are now becoming a risk factor.
Therefore, it is a priority to resurvey the mostly used routes and ports of the Baltic. In the northernmost parts of the Baltic, ice conditions may cause commercial shipping to take place outside the most commonly used routes.

## Slide 3
SEAGLE partnership
4 partners:
Institute of Aeronautics, Riga Technical University, Latvia (AERTI RTU)
Faculty of Maritime Technologies and Natural Sciences, Klaipeda University, Lithuania
Marine Systems Institute, Tallinn University of Technology, Estonia
Latvian Hydrographic Service, Maritime Administration of Latvia
Project duration: 10 months, 01.04.2016 – 31.01.2017
9

## Slide 4
AERTI RTU
Institute of Aeronautics (AERTI) was established by Riga Technical University Senate resolution in 1999, when the institute’s charter was formed after the joining of Riga Aviation University (RAU) (founded in 1919) to Riga Technical University (founded in 1862).
Institute of Aeronautics
Scientific centres
Aerospace Research and Technology Centre;
Departments
Department of Aeronautic Technologies
Department of Avionics
Department of Aircraft Theory and Construction
Department of Transport Systems and Logistics
Aviation Constructions and Space Equipment Testing Laboratory

## Slide 5
10 years of experience
Special high-technologies facilities / laboratory
Knowledge approach + practice study
Qualified professionals in RPAS field
Searching for innovations and modernization
AERTI RTU

## Slide 6: Remotely Piloted Aerial Systems – full cycle of development
1.
Research
Research of aerodynamics, construction, engineering
2.
Design & Development
Concept design, drawings, detailed component and assembly modelling using high-quality CAD design solution
3.
Manufacturing
Production process using modern CAM / CAE prototyping / production solution
4.
Evaluation & Tests
Visual evaluation of the product, analysis and tests
5.
Taking Part in Missions

## Slide 7
Fixed-wing RPAS of Micro-Class
Fixed-wing RPAS High-Endurance
Areas of activity in RPAS development

## Slide 8: LARIDAE project prototype
Gross Takeoff Weight - 25 kg
Maximum payload- 10 kg
Length – 2100 mm
Wingspan – 2500 mm
Flight range – 800 km
Flight duration up to10 h
Maximum Speed 80 km/h
Engine type – combustion
AERTI RTU

## Slide 9
1 – controller for payload
2 – table
3 – antenna tripod
4 – remote control antenna
5 – payload telemetry and live video antennas
6 – steering control antenna
7 – sun-shield
8 – ground station computer
9 – remote control
10,11 – operator chairs
RPAS GROUND STATION

## Slide 10: RPAS MANUFACTURING
Using modern materials
Carbon / Kevlar composites
Using modern technologies
3D Printer Prototyping

## Slide 11
AERTI RPAS can be equipped with following video monitoring equipment:
Video cameras
Photo cameras
Infrared camera
Thermal Camera
Other devices
AERTI RTU

## Slide 12: ICE CONDITION / AREA MONITORING

## Slide 13: PRECISION AGRICULTURE

## Slide 14: AERIAL PHOTOGRAPHY / AREA SECURITY

## Slide 15: AERTI RTU
Multi-component nano-structured coatings
Innovative ion-plasma nano-structured coatings:
Heat resistant coatings
Corrosion resistant coatings
Wear resistant coatings
Decorative coatings

## Slide 16: AERTI RTU
Research of nano-structured coatings
Multi-component heat-resisting Structure of the oxidized surface of
coating on titanium alloy titanium blade with Ti-Al-N coating

## Slide 17: AERTI RTU
Research on composite materials used for aviation constructions
In this particular project the results of research on mechanical characteristics of composite materials made of anisotropic reinforced plastics were represented. Ultimate strength and mechanical characteristics of polymer materials demand development of new testing methods which are free from traditional testing methods’ weaknesses.

## Slide 19: KLAIPEDA UNIVERSITY

## Slide 20: KLAIPEDA UNIVERSITY
KLAIPEDA UNIVERSITY

## Slide 21
KLAIPEDA UNIVERSITY

## Slide 23
HYDROGRAPHIC SERVICE
Marine surveying within Latvian waters
Supervision of aids to navigation (AtoNs)
National Coordinator for maritime safety information (MSI)
Notices to Mariners
Electronic and paper charts
Nautical Publications
Partners in Finalising Surveys for the Baltic Motorways of the Sea – FAMOS project
Maritime Administration of Latvia
23
MARITIME ADMINISTRATION OF
LATVIA

## Slide 27: In situ operational detection and monitoring of oil spills FERRYBOX system
Operated on Tallinn – Stockholm route
System operational since 2014
PAH (oil in water) sensor UVILUX integrated in July 2015
On-line data transmission and web based user interface, alarms
Performance test of PAH sensor and technology upgrade, 2015-2016
http://on-line.msi.ttu.ee/eeferry/
PAH concentration ug/l
Ferrybox system
In situ operational detection and monitoring of oil spills : FERRYBOX system
Technical specification of UVILUX
Long term variability
Hydrocarbon fluorescence. Ultraviolet dependent
spike bbetween 300 and 400 nm
Notes: According to goal of GEOILWATCH project, oil sensing sensor was integrated in the FerryBox system. The sensor should detect oil spills and remaining of the oil in surface layer of the sea, at the fairways, supported by rest of the system (data collection, primary analyses and data transmission) and to inform relevant authorities in real time.
4. Integration of UviLux UV fluorometer in FerryBox system for PAH (oil in water) (PAH - Polycyclic aromatic hydrocarbon), measurements
The UviLux is an innovative, sensitive, low cost, in-situ digital UV fluorometer providing many unique features. Variants of the UviLux enable real-time monitoring of the following parameters: Polycyclic Aromatic Hydrocarbon (PAH); Coloured Dissolved Organic Matter (CDOM); Tryptophan like fluorescence, which is a surrogate marker for Biological Oxygen Demand (BOD) and is associated with bacterial contamination in waste, recycled and natural water supplies; and Optical Brighteners used for detecting household wastewater misconnections.
4.4 Getting data from UviLux flurometer
The UviLux instrument has both analogue and digital interfaces. The digital interface is permanently enabled, but the analogue output may be enabled or disabled as required.
UviLux fluorometer signal outputs allow integration of the sensor with FerryBox system on board M/S ROMANTIKA, both through digital and analog interfaces. The data is recorded every minute, data transmission from ship into on shore FTP server also occurs with one minute interval, which allow set up the real time alert systems to all parameters and for oil contamination particularly. Settings of the GSM/GPRS modem are remotely adjustable during operation. On-line system that enables opportunity for (near) real-time observation, both, environmental parameters and system’s condition. Different parameter values are visualized operationally colour coded, additional option is display data table.
4.6 UviLux flow chamber
The Flow Chamber for UviLux fluorometer has been designed for in-line measurement applications. Incoming flow is directed across the face of the measurement window to minimize the build-up of silt while also ensuring good sample mixing. Maximum pressure in Flow Chamber is rated to 10Bar. Flow Chamber and its connections fit with existing FerryBox system on board M/S ROMANTIKA

## Slide 28
In situ operational detection and monitoring of oil spills : DRIFTERBUOY system
http://on-line.msi.ttu.ee/geoilwatch_drifter/
It’s designed robust, easy to use, autonomous drifter buoy for oil spill tracking and monitoring of surrounding environment
Surface currents, ice dynamics, water and air temperature, wave parameters and oil in water are monitored.
Equipped with GSM/GPRS two-way communication, programmable during the mission
On-line data transmission and web based user interface
Ability to collect all data to SD memory card
Validation of oil spill tracking system (SeaTrackWeb) performed
Developed by Tallinn University of Technology
PAH monitoring in single point
Construction of oil monitoring drifter

## Slide 29: Dredging impact monitoring from satellite imagery
The Central Dredging Association (CEDA Information Paper 2011) noted the following as an important lessons learned from 15 years of monitoring dredging projects: “The impacts of dredging-induced turbidity should be evaluated as an increase above background level, not as absolute values. Environmental limits should be based on the resilience of the local ecosystem, while accounting for natural fluctuations in turbidity level”.
Dredging site
Pakri ps
Pakri island
Dumping site
Global medium resolution satellite imagery provides a basis for detecting turbidity (water quality) background level in natural waterbodies from historical data in desired dredging site (where long time series of in situ measurements may be absent).
Dredging bloom
ESA Project „Environmental monitoring of harbour dredging“, in cooperation with enterprises Port of Tallinn, AS Regio

## Slide 30
HYDROGRAPHIC SERVICE
Marine surveying within Latvian waters
Supervision of aids to navigation (AtoNs)
National Coordinator for maritime safety information (MSI)
Notices to Mariners
Electronic and paper charts
Nautical Publications
Partners in Finalising Surveys for the Baltic Motorways of the Sea – FAMOS project
Maritime Administration of Latvia
30
MARITIME ADMINISTRATION OF
LATVIA

## Slide 31
Maritime Administration of Latvia
31
MARITIME ADMINISTRATION OF LATVIA - RESOURCES
«Kristians Dals»
Overall length: 19,8m
Beam: 6,7m
Draught: 1,3m
Speed: 11,0Kts
Engine: 2
Power: 324kW
Crew: 4
Multibeam: RESON SeaBat 7101
GPS: Trimble

## Slide 32
Maritime Administration of Latvia
32
MARITIME ADMINISTRATION OF LATVIA - RESOURCES
«SONĀRS»
Overall length: 7,25m
Beam: 2,4m
Draught: 0,6m
Speed: 32,0kts
Engine: 1
Power: 110,3kW
Crew: 2+1 (max.8)
Multibeam: RESON SeaBat T-20P
GPS: Trimble

## Slide 33
Maritime Administration of Latvia
33
«BLESSER»
Overall length: 6m
Beam: 2m
Engine: 2 x 50HP
Speed max: 16kts
Single beam echo sounder
MARITIME ADMINISTRATION OF LATVIA - RESOURCES

## Slide 34: SEAGLE – Main project idea - 1
The project SEAGLE propose integration of multifunctional solution of navigation fairways resurveying providing
high quality satellite and Remotely Piloted Aerial System (RPAS) data use in maritime surveillance and
remote sensing through the development of an innovative integrated monitoring system using data from RPAS and Unmanned Maritime System (UMS)
in the same time advising intelligent solutions for system command and control and advanced real-time and predictive data analytics technologies for end users.

## Slide 35: SEAGLE – Main project idea - 2

## Slide 36: SEAGLE – Main project idea - 3
Information gathered by RPAS will be used for the navigation chart data update instead of time consuming resurvey by special vessels and conventionally used satellite systems which are not always owned by National Hydrographic Service, effected by high costs and weather conditions.
RPAS being interconnected with UMS both will be used for command and control system as any of them can act as pseudo satellite for other thus providing undisturbed control of both components of proposed system.
Main task of UMS is resurvey of navigation fairways by means of payload carried within its structure. Data collected in the resurvey process from both components is transferred to the main command and control station where it can be integrated with other common systems.

## Slide 37: SEAGLE – Main project phases - 4
Phase #1. SEAGLE system definition.
In order to define SEAGLE comprehensive monitoring system for navigation fairway resurvey, this task will be based upon RPAS and UMS structural and navigational requirements analysis. Detailed analysis of State-of-the-Art of RPAS, UMS as well as advanced technologies used for their control will be carried out.
Detailed SEAGLE system model will be defined in this task through analyzing potential users' needs. SEAGLE structure and level of performance will be defined.
Additional partners to be involved: Baltic countries' hidrography services, Baltic Sea cartography services (if other than Hidrography), specialists on satellite operations and satellite data processing, specialists on Baltic Sea ground.

## Slide 38: SEAGLE – Main project phases - 2
Phase #2. SEAGLE system component integration.
The objective of this task is to link and integrate all components used for maritime surveillance. Design and integration of SEAGLE system components will be carried out through the development of command and control system for SEAGLE operation. Dealing with big data issue integrated big data management tool will be developed. Technical verification tests will be provided.
Additional partners to be involved: specialists in echo-sounding equipment sizable for UMS, additional specialists in UMS design and exploitation, specialists in avionics for RPAS and satellite data processing.

## Slide 39: SEAGLE – Main project phases - 3
Phase #3. SEAGLE system validation (virtual and real demo).
Objectives of this task is to validate SEAGLE system by mean of representative virtual operation campaigns, to validate SEAGLE system in a representative and demonstrative manner and to provide inputs and contribute to SEAGLE assessment and dissemination work packages. Real demonstration campaign will be carried out and SEAGLE complex will be validated through the real time monitoring.
Additional partners to be involved: specialists in virtual demonstrations of developed methodology, specialists in IT technologies for development of command and control software, specialists in applications for end users.

## Slide 40: SEAGLE – State-of-the-art
Relevant projects.
Speed up re-surveying of major shipping routes and ports is a project aimed to speed-up hydrographic resurveys of the Baltic Sea, and thus to contribute to improving the safety of navigation.
Finalising Surveys for the Baltic Motorways of the Sea – FAMOS. This project aims at improving safety of navigation in the Baltic Sea by increasing hydrographic survey efficiency.
Both mentioned projects aim to provide important and useful information on resurveying of Baltic Sea in more standardized manner of data collecting and the process of resurvey in a whole. Proposed project SEAGLE will study results achieved during these two projects with the main aim to integrate these results into proposed integrated monitoring system while stepping beyond state of the art in both – data collecting manner and survey process in a whole.

## Slide 41: Work plan of SEAGLE Seed Money project - 1
Output 1. State-of-play in the field addressed by the project including an overview of complementary projects
Task 1.1. Analysis of Baltic Sea need for resurvey
Task 1.2. Analysis of fairway resurvey methods used in the Baltic Sea waters and projects carried out recently and are being implemented at present.
Task 1.3. RPAS and UMS structural and navigational requirements analysis for the integration in SEAGLE system.
Task 1.4. SEAGLE system compatibles analysis with other marine systems.

## Slide 42: Work plan of SEAGLE Seed Money project - 2
Output 2. Plan for the main stage project containing: Work plan, Composition of the partnership, Budget plan
Task 2.1. Work plan development for the main project.
Task 2.2. Composing consortium for the main project.
Task 2.3. Budget plan development for the main project.
Preliminary profiles of additional partners for the main project include the following:
Baltic countries' Hidrography services, Baltic Sea Cartography services (if other than Hidrography), specialists on satellite operations and satellite data processing, specialists on Baltic Sea ground, specialists in echo-sounding equipment sizable for UMS, additional specialists in UMS design and exploitation, specialists in avionics for RPAS, specialists in virtual demonstrations of developed methodology, specialists in IT technologies for development of command and control software, specialists in applications for end users.

## Slide 43: Work plan of SEAGLE Seed Money project – target groups
Baltic countries' Hidrography services,
Baltic Sea Cartography services (if other than Hidrography),
specialists on satellite operations and satellite data processing,
specialists on Baltic Sea ground,
specialists in echo-sounding equipment sizable for UMS,
additional specialists in UMS design and exploitation,
specialists in avionics for RPAS,
specialists in virtual demonstrations of developed methodology,
specialists in IT technologies for development of command and control software,
specialists in applications for end users.

## Slide 44: Work plan of SEAGLE Seed Money project - 3
Output 3. Report on funding possibilities and steps to be taken after the seed money project is finalized
Task 3.1. Analysis of Horizon 2020 programme opportunities.
Task 3.2. Analysis of "Interreg Baltic Sea region" programme opportunities.
Task 3.3. Analysis of "BONUS Science for a Better Future of the Baltic Sea Region" programme opportunities.
Task 3.4. Analysis of "EUREKA Innovation Across Borders" programme programme opportunities.
Other programmes….

## Slide 45: Work plan of SEAGLE Seed Money project - 3
Recent relevant programmes:
Horizon 2020. Smart, green and integrated transport. MG-3.3-2016: Safer waterborne transport and maritime operations.
Bonus Blue Baltic. Strategic Objective 5: Developing improved and innovative observation and data management systems, tools and methodologies for marine information needs in the Baltic Sea region.
Interreg Baltic Sea Region. Specific Objective 3.3. Maritime Safety. The Programme wants to increase maritime safety and security based on advanced capacity of maritime organisations.

## Slide 46: SEAGLE Seed Money project first activities
Kick-off meeting held in Riga on April 15, 2016.
Consortium Agreement developed.
Partners responsibilities specified.
Next meeting to be held in Klaipeda, Lithuania in September 2016. All partners have to finalise their Output 1 State-of-play tasks. Preliminary analysis of funding sources.
Final meeting to be held in Tallinn, Estonia in December, 2016. Plan for the main stage project to be discussed. Additional partners for the main project to be involved.

## Slide 47: SEAGLE
Thank you for your attention!
Alexander Gamaleyev
mob. +371 29232885
www.aerti.rtu.lv
aleksandrs.gamalejevs@rtu.lv